## Slide 1: Computer System Architecture
Unit-1

## Slide 2: REGISTER TRANSFER LANGUAGE
A micro operations is an elementary operation performed on the information stored in one or more registers.
The result of the operation may replace the previous binary information of a register or may by transferred to another register.
The symbolic notation used to describe the micro operation transfer among registers is called a register transfer language.
The term “register transfer” implies the availability of hardware logic circuits that can perform stated micro operation and transfer the results to the operation to the same or another register.
For any function of the computer, the register transfer language can be used to describe the (sequence of) microoperations.

## Slide 3: DESIGNATION OF REGISTERS
Registers are designated by capital letters, sometimes followed by numbers (e.g., A, R13, IR)
Often the names indicate function:
  MAR - memory address register
  PC - program counter
  IR - instruction register
Registers and their contents can be viewed and represented in various ways
  A register can be viewed as a single entity:
  Registers may also be represented showing the bits of data they contain
MAR

## Slide 4: DESIGNATION OF REGISTERS
Notations and conventions:
If we intend to copy only a portion of data it is important to specify precisely where the data is located within the storage.
R1
(a) Complete Register R1
7 6 5 4 3 2 1 0
R : High Low
(b) Individual bits within R, such as R(0-7), R(15), R(L)
R2
15 0
(c) Numbering of bits in R2
PC (H) PC (L)
15 8 7 0
(d) PC register divided into a High and a Low part

## Slide 5: REGISTER TRANSFER
Register Transfer
Copying the contents of one register to another is a register transfer
A register transfer is indicated as
  R2  R1
  In this case the contents of register R1 are copied (loaded) into register R2
  A simultaneous transfer of all bits from the source R1 to the destination register R2, during one clock pulse
  Note that this is a non-destructive; i.e. the contents of R1 are not altered by copying (loading) them to R2

## Slide 6: REGISTER TRANSFER
Register Transfer
A register transfer such as
  R3  R5
  Implies that the digital system has
  the data lines from the source register (R5) to the destination register (R3)
  Parallel load in the destination register (R3)
  Control lines to perform the action

## Slide 7: CONTROL FUNCTIONS
Register Transfer
Often actions need to only occur if a certain condition is true
This is similar to an “if” statement in a programming language
In digital systems, this is often done via a control signal, called a control function
  If the signal is 1, the action takes place
This is represented as:
  P: R2  R1
  Which means “if P = 1, then load the contents of register R1 into register R2”, i.e., if (P = 1) then (R2  R1)

## Slide 8: HARDWARE IMPLEMENTATION OF CONTROLLED TRANSFERS
Implementation of controlled transfer
P: R2 R1
Block diagram
Timing diagram
Clock
Register Transfer
Transfer occurs here
R2
R1
Control
Circuit
Load
P
n
Clock
Load
t
t+1
The same clock controls the circuits that generate the control function
and the destination register
Registers are assumed to use positive-edge-triggered flip-flops

## Slide 9: SIMULTANEOUS OPERATIONS
Register Transfer
If two or more operations are to occur simultaneously, they are separated with commas
  P: R3  R5, MAR  IR
Here, if the control function P = 1, load the contents of R5 into R3, and at the same time (clock), load the contents of register IR into register MAR

## Slide 10: BASIC SYMBOLS FOR REGISTER TRANSFERS
Capital letters Denotes a register MAR, R2
& numerals
Parentheses () Denotes a part of a register R2(0-7), R2(L)
Arrow  Denotes transfer of information R2  R1
Colon : Denotes termination of control function P:
Comma , Separates two micro-operations A  B, B  A
Symbols
Description Examples
Register Transfer

## Slide 11: CONNECTING REGISTRS
Register Transfer
In a digital system with many registers, it is impractical to have data and control lines to directly allow each register to be loaded with the contents of every possible other registers
To completely connect n registers  n(n-1) lines
O(n2) cost
  This is not a realistic approach to use in a large digital system
Instead, take a different approach
Have one centralized set of circuits for data transfer – the bus
Have control circuits to select which register is the source, and which is the destination

## Slide 12: BUS AND BUS TRANSFER
Bus is a path(of a group of wires) over which information is transferred, from any of several sources to any of several destinations.
From a register to bus: BUS  R
Register A
Register B
Register C
Register D
Bus lines
Bus and Memory Transfers

## Slide 13: Three-State Buffers
3-state bus buffers are often used at the outputs of storage flip-flops.
  Essentially, the buffer unit “holds” the value stored in the FF.
  Holding is useful for synchronizing enabling of parallel circuits
The buffer unit can be used along with a Decoder unit as a replacement for an address multiplexer.
  This is an alternative approach.
R0
R1
R2
R3
2x4
DEC
(K)
0
1
2
3
S0
S1
E
Select
Enable
{
Bus line for bit K

## Slide 14: Three-State Buffers
3-state bus buffers are often used at the outputs of storage flip-flops.
  Essentially, the buffer unit “holds” the value stored in the FF.
  Holding is useful for synchronizing enabling of parallel circuits
The buffer unit can be used along with a Decoder unit as a replacement for an address multiplexer.
  This is an alternative approach.
R0
R1
R2
R3
2x4
DEC
(K)
0
1
2
3
S0
S1
E
Select
Enable
{
Bus line for bit K

## Slide 15: Three-State Buffers
3-state bus buffers are often used at the outputs of storage flip-flops.
  Essentially, the buffer unit “holds” the value stored in the FF.
  Holding is useful for synchronizing enabling of parallel circuits
The buffer unit can be used along with a Decoder unit as a replacement for an address multiplexer.
  This is an alternative approach.
R0
R1
R2
R3
2x4
DEC
(K)
0
1
2
3
S0
S1
E
Select
Enable
{
Bus: R2(K)
0
1
1

## Slide 16: Using Tri-state buffers and the decoder construct a bus system to transfer information from four registers. Each register is 4-bit wide.

## Slide 17: BUS TRANSFER IN RTL
Bus and Memory Transfers
Depending on whether the bus is to be mentioned explicitly or not, register transfer can be indicated as either
or
In the former case the bus is implicit, but in the latter, it is explicitly indicated
R2 R1
BUS R1, R2  BUS

## Slide 18: MEMORY (RAM)
Bus and Memory Transfers
Memory (RAM) can be thought as a sequential circuits containing some number of registers
These registers hold the words of memory
Each of the r registers is indicated by an address
These addresses range from 0 to r-1
Each register (word) can hold n bits of data
Assume the RAM contains r = 2k words. It needs the following
  n data input lines
  n data output lines
  k address lines
  A Read control line
  A Write control line
data input lines
data output lines
n
n
k
address lines
Read
Write
RAM
unit

## Slide 19: MEMORY TRANSFER
Bus and Memory Transfers
Collectively, the memory is viewed at the register level as a device, M.
Since it contains multiple locations, we must specify which address in memory we will be using
This is done by indexing memory references
Memory is usually accessed in computer systems by putting the desired address in a special register, the Memory Address Register (MAR, or AR)
When memory is accessed, the contents of the MAR get sent to the memory unit’s address lines
AR
Memory
unit
Read
Write
Data in
Data out
M

## Slide 20: MEMORY READ
Bus and Memory Transfers
To read a value from a location in memory and load it into a register, the register transfer language notation looks like this:
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Read (= 1) gets sent to the memory unit
  The contents of the specified address are put on the memory’s output data lines
  These get sent over the bus to be loaded into register R1
R1  M[MAR]

## Slide 21: MEMORY WRITE
Bus and Memory Transfers
To write a value from a register to a location in memory looks like this in register transfer language:
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Write (= 1) gets sent to the memory unit
  The values in register R1 get sent over the bus to the data input lines of the memory
  The values get loaded into the specified address in the memory
M[MAR]  R1

## Slide 22: SUMMARY OF R. TRANSFER MICROOPERATIONS
Bus and Memory Transfers
A  B Transfer content of reg. B into reg. A
AR DR(AD) Transfer content of AD portion of reg. DR into reg. AR
A  constant Transfer a binary constant into reg. A
ABUS  R1, Transfer content of R1 into bus A and, at the same time,
R2 ABUS transfer content of bus A into R2
AR Address register
DR Data register
M[R] Memory word specified by reg. R
M Equivalent to M[AR]
DR  M Memory read operation: transfers content of
memory word specified by AR into DR
M  DR Memory write operation: transfers content of
DR into memory word specified by AR

## Slide 23: MICROOPERATIONS
Computer system microoperations are of four types:
- Register transfer microoperations
- Arithmetic microoperations
- Logic microoperations
- Shift microoperations
Arithmetic Microoperations

## Slide 24: ARITHMETIC MICROOPERATIONS
Summary of Typical Arithmetic Micro-Operations
Arithmetic Microoperations
  R3  R1 + R2 Contents of R1 plus R2 transferred to R3
  R3  R1 - R2 Contents of R1 minus R2 transferred to R3
  R2  R2’ Complement the contents of R2
  R2  R2’+ 1 2's complement the contents of R2 (negate)
  R3  R1 + R2’+ 1 subtraction
  R1  R1 + 1 Increment
  R1  R1 – 1 Decrement
The basic arithmetic microoperations are
  Addition
  Subtraction
  Increment
  Decrement
The additional arithmetic microoperations are
  Add with carry
  Subtract with borrow
  Transfer/Load
  etc. …

## Slide 25: BINARY ADDER
A binary adder is a digital circuit that produces the arithmetic sum of two binary numbers.
A binary adder can be constructed with full adders connected in cascade with the output carry form each full adder connected to the input carry of the next full adder in the chain.
The four-bit adder is a typical example of a standard component .It can be used in many application involving arithmetic operations.
The input carry to the adder is C0and it ripples through the full adders to the output carry C4 .
n-bit binary adder requires n full adders.

## Slide 26: BINARY ADDER

## Slide 27: BINARY ADDER
The addition A+B of binary numbers in parallel implies that all the bits of A and B are available for computation at the same time.
As in any combinational circuit, the signal must propagate through the gates before the correct output sum is available.
The output will not be correct unless the signals are given enough time to propagate through the gates connected form the input to the output.
The longest propagation delay time in an adder is the time it takes the carry to propagate through the full adders.

## Slide 28: Binary Adder-Subtractor
Subtraction of A – B can be done by taking 2’s complement of B and added to A. The 2’s complement can be done by taking 1’s complement then adding “1” to the result.
And finally the 1’s complement is the binary inversion.

## Slide 29: Binary Adder-Subtractor
The addition and subtraction operations can be combined into one common circuit by including Ex-OR with each full adder.
The mode bit M controls the operations.
When M=0 the circuit is adder and when M=1 circuit becomes a subtractor.
Each X-OR gate receives input M and one of the input B.
When M=0, we have B . 0=B the full adders receive the value of B, the input carry 0 and circuit performs A+B.
When M=1 we have B 1=B’ and carry=1. The B input all are complemented a 1 is added through the input carry.
The circuit performs the operation A+2’s complement of B.

## Slide 30: Incrementer
The binary incrementer increases the value stored in a register by ‘1’.
For this, it simply adds ‘1’ to the existing value stored in a register.
It is made by cascading ‘n’ half adders for ‘n’ number of bits i.e. the storage capacity of the register to be incremented.
Hence, a 4-bit binary incrementer requires 4 cascaded half adder circuits.

## Slide 31: Binary Decrementer
Binary decrementer decrease the register value by 1.
Decrement can be achieved by taking 2’s complement of 1 and adding to A.
A – 1 = A + 2’s complement of 1 = A + 1111

## Slide 32: ARITHMETIC CIRCUIT
The arithmetic micro operations listed in table can be implemented in one composite arithmetic circuit.
This circuit comprised of full adders and multiplexers. The multiplexer controls which data is fed into Y input of the adder.
The output of the binary adder is computed from
D = A + Y +Cin
The Y input can have one of 4 different values: B, B’, always “1”, or always “0”.

## Slide 33: ARITHMETIC CIRCUIT

## Slide 34: ARITHMETIC CIRCUIT
Arithmetic Microoperations

## Slide 35: ARITHMETIC CIRCUIT
Case 1: When S1 S0=0 0
Cin =0 then output D= A+B
Cin = 1 then output D=A+B+1
Both cases perform add micro operation with or without adding input carry.
Case 2: S1 S0 =01 the complement of B is applied to the y inputs of the adder.
If Cin=1 then D= A + B’ +1 =>A - B
Cin = 0 then D= A + B’ => A – B- 1
Case 3: S1 S0= 10 all zero’s are inserted into the y inputs.
If Cin = 0 then the output D= A + 0 + 0 => A
Cin = 1 then the output D= A+1
In a first case we have a direct transfer from input A to output D. in the second case, the value of A is incremented by 1.
Case 1 : When S1 S0 =11 all the one’s are inserted into the Y inputs.
If Cin = 0 then output D= A+ all 1’s
D= A+ ( 2’s Complement of 1)
D= A - 1
Cin= 1 then output D = A- 1- 1 = A
Which causes a direct transfer from input A to output D.

## Slide 36: LOGIC MICROOPERATIONS
Logic micro operations specify binary operations on the strings of bits in registers. Logic micro operations are bit-wise operations, i.e., they work on the individual bits of data.
Most systems only implement four of these:
AND ( ), OR ( ), XOR ( ), Complement/NOT

## Slide 37: LOGIC MICROOPERATIONS

## Slide 38: HARDWARE IMPLEMENTATION OF LOGIC MICROOPERATIONS
0 0 F = A  B AND
0 1 F = AB OR
1 0 F = A  B XOR
1 1 F = A’ Complement
S1 S0
Output
-operation
Function table
Logic Microoperations
B
A
S
S
F
1
0
i
i
i
0
1
2
3
4 X 1
MUX
Select

## Slide 39: APPLICATIONS OF LOGIC MICROOPERATIONS
Logic Microoperations
Logic microoperations can be used to manipulate individual bits or a portions of a word in a register
Consider the data in a register A. In another register, B, is bit data that will be used to modify the contents of A
  Selective-set A  A + B
  Selective-complement A  A  B
  Selective-clear A  A • B’
  Mask (Delete) A  A • B
  Clear A  A  B
  Insert A  (A • B) + C
  Compare A  A  B

## Slide 40: SELECTIVE SET
Logic Microoperations
The selective-set operation sets to 1 the bits in register A where there are corresponding 1’s in register B.
it does not affect bit positions that have 0’s in B. the following numerical example clarifies this operation:-
1010 A before
1100 B (logic operand)
1110 A after

## Slide 41: SELECTIVE COMPLEMENT
Logic Microoperations
The selective-complement operation complements bits in register A where there are corresponding 1’s in register B. it does not affect bit positions that have 0’s in B.
The following numerical example clarifies this operation:-
1010 A before
1100 B (logic operand)
0110 A after

## Slide 42: SELECTIVE CLEAR
Logic Microoperations
The selective-clear operation clears to 0 the bits in register A only where there are corresponding 1’s in register B. For example:-
1010 A before
1100 B (logic operand)
0010 A after

## Slide 43: MASK OPERATION
Logic Microoperations
The mask operation is similar to the selective-clear operation except that the bits of A are cleared only where there are corresponding 0’s in B. the mask operation is an AND micro operation, for example:-
1010 A before
1100 B (logic operand)
1000 A after masking

## Slide 44: CLEAR OPERATION
Logic Microoperations
The clear operation compares the words in A and B and produces an all 0’s result if the two numbers are equal.
This operation is achieved by an exclusive-OR microoperation as has own by the following example:
1010 A
1010 B
0000 A A B
When A and B are equal, the two corresponding bits are either both 0 or both 1. in either case the exclusive-OR operation produces a 0.
The all-0’s result is then checked to determine if the tow numbers were equal.

## Slide 45: INSERT OPERATION
Logic Microoperations
The insert operation inserts a new value into a group of bits. This is done by first masking the bits and then Oring them with the required value.
For example, suppose that an A register contains eight bits, 0110 1010. to replace the four leftmost bits by the value 1001 we first the four unwanted bits:-
0110 1010 A before
0000 1111 B (mask)
0000 1010 A after masking
and then insert the new value:-
0000 1010 A before
1001 0000 B (insert)
1001 1010 A after insertion
The mask operation is an AND microoperation and the insert operation is an OR microoperation.

## Slide 46: Shift Microoperations
Shift Microoperations are used for serial transfer of data.
They are also used for conjunction with arithmetic, logic and other data-processing operations.
Shift operations can be done on registers.
The content of registers can be shifted to the left or to the right.
A logical shift is one that transfers 0 through the serial inputs.

## Slide 47: Shift Microoperations
In shift left operation the serial input transfers a bit Contents of register into the right most position.
In shift right operation the serial input transfers a bit Contents of register into the left most position.
Shift Microoperations | 
Symbolic | Descriptive
R = shl R | Shift-left logical register R
R = shr R | Shift-right logical register R
R = cil R | Circular shift-left register R
R = cir R | Circular shift-right register R
R = ashl R | Shift-left arithmetic register R
R = ashr R | Shift-right arithmetic register R

## Slide 48: Shift Microoperations
Shift Microoperations | 
Symbolic | Descriptive
R = shl R | Shift-left logical register R
R = shr R | Shift-right logical register R
R = cil R | Circular shift-left register R
R = cir R | Circular shift-right register R
R = ashl R | Shift-left arithmetic register R
R = ashr R | Shift-right arithmetic register R
High order
Input 0
Shift right
Low Order
Bit Loss
High order
Bit Loss
Shift left
Low Order
Input 0

## Slide 49: Shift Microoperations
In circular shift circulate the bit of register around the two ends without loss of information.
Shift Microoperations | 
Symbolic | Descriptive
R = shl R | Shift-left logical register R
R = shr R | Shift-right logical register R
R = cil R | Circular shift-left register R
R = cir R | Circular shift-right register R
R = ashl R | Shift-left arithmetic register R
R = ashr R | Shift-right arithmetic register R
High order
From Low order
Circular shift right
Low order
to High order
High order
to Low order
Circular shift left
Low order
from High order

## Slide 50: Shift Microoperations
An arithmetic shift is a microoperation that shifts a signed binary number to the left or right.
An arithmetic shift left multiplies a signed number by 2.
An arithmetic shift right divides a signed number by 2.
Shift Microoperations | 
Symbolic | Descriptive
R = shl R | Shift-left logical register R
R = shr R | Shift-right logical register R
R = cil R | Circular shift-left register R
R = cir R | Circular shift-right register R
R = ashl R | Shift-left arithmetic register R
R = ashr R | Shift-right arithmetic register R
High order
Bit Loss
Arithmetic shift left
Low Order
Input 0
High order
Input High order
Arithmetic shift right
Low order
Bit Loss

## Slide 51: Shift Microoperations
The arithmetic shift right leaves the sign bit unchanged and shift the number(including the sign bit) to the right.
The Rn-1 remains the same, Rn-2 receives the bit from Rn-1 and so on for the other bits of the register. The bit in R0 is lost.
The arithmetic shift-left inserts a 0 in R0, and shift all other bits to the left.
The initial bit Rn-1 is lost and replace by Rn-2. A sign reversal occurs if the bit in Rn-1 changes in value after the shift.

## Slide 52: Shift Microoperations
If the bits Rn-1 and Rn-2 are not same then overflow will occur.
An overflow flip-flop Vs can be used to detect an arithmetic shift-left overflow
Vs = Rn-1  Rn-2
Rn-2
Vs=
Rn-1
1  overflow
0  no overflow

## Slide 53: Hardware Implementation of logic microoperations

## Slide 54: Arithmetic Logic Shift Unit
Instead of having individual registers performing the microoperations directly, computer systems employ a number of storage registers connected to a common operational unit called an Arithmetic Logic Unit (ALU)

## Slide 55: Arithmetic Logic Shift Unit

## Slide 56: Arithmetic Logic Shift Unit