## Slide 1: Introduction
Ad Hoc Network is a multi-hop relaying network
ALOHAnet developed in 1970
Ethernet developed in 1980
In 1994, Bluetooth proposed by Ericsson to develop a short-range, low-power, low- complexity, and inexpensive radio inteface
WLAN 802.11 spec. is proposed in 1997

## Slide 2: Cellular and Ad Hoc Wireless Networks
Cellular Wireless Networks: infrastructure dependent network
Ad Hoc Networks: multi-hop radio relaying and without support of infrastructure
  Wireless Mesh Networks
  Wireless Sensor Networks

## Slide 3
Cellular Wireless Networks
Hybrid Wireless Networks
Wireless Mesh Networks
Wireless Sensor Networks
Infrastructure Dependent (Single-Hop Wireless Networks)
Ad Hoc Wireless Networks (Multi-Hop Wireless Networks)
Figure Cellular and ad hoc wireless networks.

## Slide 4
B
A
C
D
E
Switching Center
+
Gateway
Path from C to E
Base Station Mobile Node
Figure A cellular networks.
5

## Slide 5
B
A
C
F
D
E
Path from C to E
Mobile Node Wireless Link
Figure. An ad hoc wireless networks
6

## Slide 6: Differences between cellular networks and ad hoc wireless networks
Cellular Networks | Ad Hoc Wireless Networks
Fixed infrastructure-based | Infrastructure-less
Single-hop wireless links | Multi-hop wireless links
Guaranteed bandwidth (designed for voice traffic) | Shared radio channel (more suitable for best-effort data traffic)
Centralized routing | Distributed routing
Circuit-switched (evolving toward packet switching) | Packet-switched (evolving toward emulation of circuit switching)
Seamless connectivity (low call drops during handoffs) | Frequency path break due to mobility
High cost and time of deployment | Quick and cost-effective deployment
Reuse of frequency spectrum through geographical channel reuse | Dynamic frequency reuse based on carrier sense mechanism
7

## Slide 7: Differences between cellular networks and ad hoc wireless networks (cont.)
Easier to achieve time synchronization | Time synchronization is difficult and consumes bandwidth
Easier to employ bandwidth reservation | Bandwidth reservation requires complex medium access control protocols
Application domains include mainly civilian and commercial sector | Application domains include battlefields, emergency search and rescue operation, and collaborative computing
High cost of network maintenance (backup power source, staffing, etc.) | Self-organization and maintenance properties are built into the network
Mobile hosts are of relatively low complexity | Mobile hosts require more intelligence (should have a transceiver as well as routing/switching capacity)
Major goals of routing and call admission are to maximize the call acceptance ratio and minimize the call drop ratio | Man aim of routing is to find paths with minimum overhead and also quick reconfiguration of broken paths
Widely deployed and currently in the third generation | Several issues are to be addressed for successful commercial deployment even though widespread use exists in defense
8

## Slide 8: Applications of Ad Hoc Wireless Networks
Military Applications
  Establishing communication among a group of soldiers for tactical operations
  Coordination of military object moving at high speeds such as fleets of airplanes or ships
  Requirements: reliability, efficiency, secure communication, and multicasting routing,
Collaborative and Distributed Computing
  Conference, distributed files sharing
Emergency Operations
  Search, rescue, crowd control, and commando operations
  Support real-time and fault-tolerant communication paths

## Slide 9: Wireless Mesh Networks
An alternate communication infrastructure for mobile or fixed nodes/users
Provides many alternate paths for a data transfer session between a source and destination
Advantages of Wireless Mesh Networks
– High data rate, quick and low cost of deployment, enhanced services, high scalability, easy extendability, high availability, and low cost per bit

## Slide 10
A house with rooftop transceiver
Transmission range
Wired link to the Internet
Wireless link
Figure 5.4. Wireless mesh networks operating in a residential zone
Wired Network
Gateway node

## Slide 11: Internet
Wired link to the Internet
Multi-hop radio relay link
Lamp
Radio relay node
Figure 5.5 Wireless mesh network covering a highway
Coverage area

## Slide 12: Wireless Sensor Networks
A collection of a large number of sensor nodes that are deployed in a particular region
Applications:
  military, health care, home security, and environmental monitoring
Differences with the ad hoc wireless networks:
  Mobility of nodes, size of network, density of deployment, power constraints, data/information fusion, traffic distribution

## Slide 13: Hybrid Wireless Networks
HWN such as Multi-hop cellular networks and integrated cellular ad hoc relay networks
  The base station maintains the information about the topology of the network for efficient routing
  The capacity of a cellular network can be increased if the network incorporates the properties of multi-hop relaying along with the support of existing fixed infrastructure
Advantages:
  Higher capacity than cellular networks due to better channel reuse
  Increased flexibility and reliability in routing
  Better coverage and connectivity in holes

## Slide 14
Switching Center
+
Gateway
B
A
C D
E
MCN communication
Base Station Mobile Node
Figure 5.6. MCN architecture.

## Slide 15: Issues in Ad Hoc Wireless Networks
Medium access scheme
Routing, Multicasting, TPC protocol
Pricing scheme, QoS, Self-organization
Security, Energy management
Addressing and service discovery
Deployment considerations

## Slide 16: Medium Access Scheme
Distributed operation
  fully distributed involving minimum control overhead
Synchronization
  Mandatory for TDMA-based systems
Hidden terminals
  Can significantly reduce the throughput of a MAC protocol
Exposed terminals
  To improve the efficiency of the MAC protocol, the exposed nodes should be allowed to transmit in a controlled fashion without causing collision to the on-going data transfer
Access delay

## Slide 17: The Major Issues of MAC Scheme
Throughput and access delay
  To minimize the occurrence of collision, maximize channel utilization, and minimize controloverhead
Fairness
  Equal share or weighted share of the bandwidth to all competing nodes
Real-time traffic support
Resource reservation
  Such as BW, buffer space, and processing power
Capability for power control
Adaptive rate control
Use of directional antennas
18

## Slide 18: The Major Challenge of Routing Protocol
Mobility result in frequent path break, packet collision, and difficulty in resource reservation
Bandwidth constraint: BW is shared by every node
Error-prone and share channel: high bit error rate
Location-dependent contention: distributing the network load uniformly across the network
Other resource constraint: computing power, battery power, and buffer storage

## Slide 19: The Major Requirement of Routing Protocol
Minimum route acquisition delay
Quick route reconfiguration: to handle path breaks
Loop-free routing
Distributed routing approach
Minimum control overhead
Scalability
Provisioning of QoS:
  supporting differentiated classes of services
Support for time-sensitive traffic
Security and privacy

## Slide 20: The Major Issues in Multicast Routing Protocols
Robustness
  recover and reconfigure quickly from link breaks
Efficiency
  minimum number of transmissions to deliver a data packet to all the group members
Minimal Control overhead
QoS support
Efficient group management
Scalability
Security

## Slide 21: Transport Layer Protocols
Objectives: setting up and maintaining
  End-to-end connections, reliable end-to-end data delivery, flow control, and congestion control
Major performance degradation:
  Frequent path breaks, presence of old routing information, high channel error rate, and frequent network partitions

## Slide 22: Quality of Service Provisioning
QoS often requires negotiation between the host and the network, resource reservation schemes, priority scheduling and call admission control
QoS in Ad hoc wireless networks can be on a per flow, per link, or per node
Qos Parameters: different applications have different requirements
  Multimedia: bandwidth and delay are the key parameters
  Military: BW, delay, security and reliability
  Emergency search –and-rescue: availability is the key parameters, multiple link disjoint paths
  WSN: battery life, minimum energy consumption

## Slide 23: Quality of Service Provisioning
QoS-aware routing:
  To have the routing use QoS parameters for finding a path
  The parameters are network through put, packet delivery ratio, reliability, delay, delay jitter, packet lost rate, bit error rate, and path loss
QoS framework:
  A frame work for QoS is a complete system that attempts to provide the promised service
  The QoS modules such as routing protocol, signaling protocol, and resource management should react promptly according to changes in the network state

## Slide 24: Self-Organization
An important property that an ad hoc wireless network should exhibit is organizing and maintaining the network by itself
Major activities: neighbor discovery, topology organization, and topology reorganization
Ad hoc wireless networks should be able to perform self-organization quickly and efficiently

## Slide 25: Security
The attack against ad hoc wireless networks are classified into two types: passive and active attacks
Passive attack: malicious nodes to observe the nature of activities and to obtain information in the network without disrupting the operation
Active attack: disrupt the operation of the network
  Internal attack: nodes belong to the same network
  External attack: nodes outside the network